## Slide 1: Problem Solving Schools Geology Challenge 2021

## Slide 2
Town of approximately 25000 residents; administrative centre for wider district of c.60000 people
We need you to build a hydropower facility for Anningville!
Welcome to sunny Anningville!

## Slide 3
An overview to hydropower plants and Dams
Explain your task and how to complete it
Questions
Resource pack is available
Welcome to sunny Anningville!

## Slide 4
Renewable energy resource
Conversion of energy from flowing water to electricity.
We will be focussing on conventional hydroelectric plants
  Concrete structure (dam) is built across a river valley
  This creates a large artificial lake (reservoir)
  The reservoir is used to store water, which is passed through a turbine in the dam, producing electricity as it turns.
What is hydropower?
RESERVOIR
DAM
RIVER

## Slide 5
What is hydropower?
RESERVOIR
DAM
RIVER
Renewable energy resource
Conversion of energy from flowing water to electricity.
We will be focussing on conventional hydroelectric plants
  Concrete structure (dam) is built across a river valley
  This creates a large artificial lake (reservoir)
  The reservoir is used to store water, which is passed through a turbine in the dam, producing electricity as it turns.

## Slide 6
Where can we build dams?
The most suitable sites for dams are narrow river valleys or canyons. This allows a relatively small dam to be built, but large volumes of water to be held.

## Slide 7
What geology is suitable?
The geology of the dammed valley is critically important.
Siting a dam on unsuitable rocks can allow water to leak from the reservoir, make the dam unstable or even lead to its failure.

## Slide 8
What geology is suitable?
Rock type
Rocks should be impermeable, i.e., they do not let water flow through them.
Most igneous rocks (e.g. granite, gabbro)
Some metamorphic rocks, such as gneiss and quartzite
Massive, well-cemented quartz sandstone

## Slide 9
What geology is suitable?
Rock type
Rocks should not dissolve in water. Rocks with a high CaCO3 content are unsuitable, including:
Limestone
Marble
Sedimentary rocks cemented with calcite (CaCO3)

## Slide 10
What geology is suitable?
Structure
Faults and joints can make rocks permeable, by creating cracks for water to migrate through.
The effects of these can be mitigated with concrete grouting, where concrete is injected at high pressures to fill the gaps.
Dams should not be built near large-scale active faults – grouting will not help if there is an earthquake!

## Slide 11
What geology is suitable?
Sedimentary rocks usually build up in layers; these layers can be horizontal, or they can tilt (dip) in different directions.

## Slide 12
What geology is suitable?
Sometimes, dipping beds can be highly beneficial to dam construction. At other times, they can be dangerous.
It all depends on the direction of the dip.
Reservoir
Dam
Top of valley
Reservoir
Dam
Top of valley
Reservoir
Dam
Top of valley
Beds dipping upstream
Horizontal beds
Beds dipping downstream

## Slide 13
What geology is suitable?
Layers (beds) of rock can dip in different directions. Sometimes the dip can be highly beneficial to dam construction, others not.
Beds dipping into valley
Dam
Bedding strike is across the valley
Dam

## Slide 14
Suitable Geology: Summary
Rocks should be impermeable
Rocks should not dissolve in water
Rocks should not be excessively fractured by faults or joints
If the rocks are no longer actively being fractured, e.g. by an active fault, concrete grouting can be applied to make a site suitable
Rock beds should not dip downstream of the dam
Rock beds should not dip into the valley that holds the reservoir.

## Slide 15
Advantages of hydropower use:
Renewable energy resource
Expensive to set up, but cheap to produce energy once running
Potential to mitigate flooding
Water storage for dry seasons
Minimal CO2 emissions
Flexible energy supply – release more water when demand for power is higher

## Slide 16
Disadvantages of hydropower use:
Large areas are flooded to create reservoirs
Loss of homes or habitat incurred
Dams can block important sediment transport down rivers, leading to significant erosion downstream
Dams may block important migration routes for aquatic wildlife
Significant methane release when forested areas are flooded

## Slide 17
Your challenge…
.

## Slide 18
Town of approximately 25000 residents; administrative centre for wider district of c.60000 people
Local industry was formerly farming and fishing, due to wide flat plain on which the town is built
Main industry now is tourism.
Welcome to sunny Anningville!

## Slide 19
Threat from climate warming; Anningville has experienced 3 exceptional flooding events in the last 12 years
Cause identified as higher than average glacial meltwater levels in the spring, combined with seasonal storms.
State-wide, the area is suffering from prolonged periods of drought in the summer
Welcome to sunny Anningville!

## Slide 20: Welcome to sunny Anningville!
Local government has created new “climate charter”
Commitment to use 100% renewable energy in the local grid within 20 years.
Hydropower is preferred source; abundant availability of water in region, minimal CO2 output, and option of storing water for summer months

## Slide 21: Your task…
Six potential sites have been identified for dams. You need to:
Identify which sites are geologically suitable
Choose where to build your dam(s)
Propose a budget for the project
Convince Anningville Town Council (aka the judges) that your team should be contracted to build the hydropower plant(s)!
You are contractors vying for the rights to construct and supply hydropower facilities to Anningville.

## Slide 24: Resources to help you:
You will have access to a Google or DropBox folder with the following:
A brief and a copy of this presentation
A satellite map of the area, showing the six potential dam sites
A geological map of the area
A detailed overview of each site
A sheet to help you calculate your budget

## Slide 25: How this will be assessed
You have just over 1 hour to decide where to build your dam(s), complete a budget, and prepare a presentation.
During this time, you will complete a budget via Google Sheets, and a summary of your decisions via Google Forms
After you have submitted your budget and summary, you will be called in a random order to pitch to the judges. You will have 3 minutes to tell them which site(s) you chose, why you chose them and why they should choose your team to build the hydropower plant(s).

## Slide 26: Resources to help you:
Budget
Part of the assessment is the budget you produce for your project, and how wisely you spend money
All the information you need for this is on the budgeting sheet
The maximum you can spend is £950 million; marks are not gained for saving money!
You have the opportunity to “buy” information from an external contractors, if you would like to.

## Slide 27: Finally, some tips…
There are suggested timings to complete this activity in the Brief – make sure you read them!
There are some wrong answers, but there is more than one “right” answer. Decide which is the best option as a team; use prior knowledge, common sense, and the information given to you
3 minutes is not long for a presentation. Highlight the information which is most important!